## Slide 1: Far-forward detector at EicC
Aiqiang Guo, Yutie Liang, Ting Lin, Weizhi Xiong
2023.01.18

## Slide 2
Outline
Review of far-forward detector design
Recent updates
Summary

## Slide 3
Far-forward Detector design based on dipoles
EDT (Endcap Dipole Tracking)
FDT (Forward Dipole Tracking)
Four disks with pixel size of 10 μm same as the central vertex detector
ZDC(Zero Degree Calorimeter)
OMD(Off-Momentum Detector)
Notes: Previously，we have designed the forward tracking detector, utilizing the 1st and 2nd dipoles.
There are two detector sets, one is named EDT (Endcap Dipole Tracker) and the other is FDT (Forward Dipole tracker).
Both EDT and FDT are designed with 4 disks with pixel size of 10 um same as the central vertex detector.

## Slide 4
L=0.8m
Dipole 3: z = 15.4 m B = -3.4 T L = 0.8 m
R2 = p*10/3./B2 = 20GeV*10/3./2.69 = 19.61 m
Bending angle = asin(L/R) ~ 0.04 rad = 40 mrad
30 mrad
A
B
O
L=2.0m
C
D
R3
= 19.61m
R1
= 26.455m
Dipole 1: z = 5 m B = 2.52 T L = 0.8 m
R1 = p*10/3./B1 = 20GeV*10/3./2.52 = 26.455 m
Bending angle = asin(L/R) = 0.03 rad = 30 mrad
50 mrad
50 mrad
40 mrad
Dipoles in the ion forward direction
30 mrad
50 mrad
80 mrad
R2
= 24.783m
120 mrad
Dipole 2: z = 10 m B = 2.69 T L = 2.0 m
R2 = 24.783 m
Bending angle = 80 mrad
Dipole 4: z > 16 m B = ? L = ? m
R2 = ? m
Bending angle = 120 mrad
4

## Slide 5
EDT
FDT
mrad : DVCS ratio relative to 2 mrad
16-34: 9.3%
16-60: 9.9%
5-16: 45.3%
2-5： 44.7%
ZDC: 15 mrad
FDT: 5-16 mrad
From Weizhi
EDT: 16-60 mrad
Far-forward detectors
Notes: One of the main physics focus of the forward detector is the measurement of DVCS process.
In the whitepaper, the DVCS process was investigated with a cut of theta_p_prime (the angle between scatter proton and the original proton beam) larger than 2 mrad.
In our first Forward detector design, EDT has a coverage of 16-60 mrad with the DVCS acceptance of 9.9% (relative to 2 mrad cut)
FDT has a coverage of 5-16 mrad, with the DVCS acceptance of 45.3% (relative to 2 mrad cut)
A combination of EDT and FDT may recover more than 55% of the DVCS events.

## Slide 6
Recent updates
-- Quadrupoles magnets

## Slide 7
Quadrupoles in the ion forward direction
Slides from Weizhi

## Slide 8
L=0.8m
30 mrad
A
B
O
R1 = 26.455m
50 mrad
50 mrad
Position of B(-28.1453, 0, 538.6）
Position of Q1(-36.1368, 0, 638.3）
Position of Q2(-40.9317, 0, 698.1）
Position of Q3(-52.5193, 0, 842.6）
Q1
Q2
L=0.4m
L=1.1m
Q3
L=0.6m
0.1m
0.6m
0.8m
Quadrupoles in the ion forward direction
Dipole 1: z = 5 m B = 2.52 T L = 0.8 m
R1 = 26.455 m
Bending angle = 30 mrad
Dipole 2: z = 10 m B = 2.69 T L = 2.0 m
R2 = 24.783 m
Bending angle = 80 mrad

## Slide 9
Impact of Quadrupoles
DIPOLE
DIPOLE+QUAD

## Slide 10
Impact of Quadrupoles
n_EDT > 1 DIPOLE
n_EDT > 1 DIPOLE+QUAD
n_FDT > 1 DIPOLE
n_FDT > 1 DIPOLE+QUAD

## Slide 11
Phi=90
Impact of Quadrupoles
Phi=0
Theta = [0 - 60] mrad
Phi=180
Phi=270
Low acceptance below 10 mrad !
Low acceptance below 10 mrad !

## Slide 12
Theta = 10 mrad DIPOLE
Theta = 10 mrad DIPOLE+QUAD / vacuum
Theta = 10 mrad DIPOLE+QUAD + beampipe
Impact of Quadrupoles
Z=700cm
Z=800cm
Z=1500cm
phi=0
phi=90
phi=180
phi=270

## Slide 13
Impact of Quadrupoles -- Acceptance
Previously with only DIPOLE
DIPOLE and QUAD

## Slide 14
Impact of Quadrupoles -- resolution
To-do: extrapolate back to the IP!

## Slide 15
Impact of stronger quadrupole fields
Current QUAD
Current QUAD
QUAD increase by 50%
QUAD increase by 50%

## Slide 16
Summary and next-to-do
Design of EDT FDT and ZDC in FF is good shape.
Impact of three quadrupole magnets is investigated.
  strong azimuthal dependency on the FDT
  a reduction on the tracking efficiency
  resolution? need to extrapolate back to IP
Far-forward OMD design is ongoing.
Thank you

## Slide 19
Theta = 10 mrad Phi = 145-150 DIPOLE
Theta = 10 mrad Phi = 145-150 DIPOLE+QUAD

## Slide 21
Theta = 10 mrad Phi = 145-150 DIPOLE+QUAD
Theta = 10 mrad Phi = 145-150 DIPOLE
All Vacuum

## Slide 22
0o
x
y
z
90o
180o
270o

## Slide 23
Impact of Quadrupoles -- resolution
Genfit in EiccRoot need to be tuned.
Mean value shift
Resolution could be better
Track is not extrapolated back to the IP!