## Slide 1: MRPC和量能器-高精度时间和能量测量
Yi Wang
Department of Engineering Physics
Tsinghua University

## Slide 2: Outline
Introduction of MRPC and Shashlyk ECAL
Future requirement for MRPC-TOF:
-- High rate >20kHz/cm2
-- High time resolution <20ps
-- Use sealed MRPC to reduce gas consumption
-- Find Eco-friendly working gas
Development of Ecal for NICA/MPD
五维Shshlyk型ECAL的概念设计
Summary

## Slide 3: MRPC introduction
Application in nuclear physics experiments
Application in industry（Muon tomography)
Application in medicine（TOF-PET）
Read out
Read out
Insulator
Carbon
Insulator
Resistive
plate
MRPC application：
MRPC structure
主要优点:
时间分辨达到： 几十ps量级
探测效率：>98%
造价便宜
长期工作稳定！
Honey
PCB
Mylar
Graphite
Fish line
Glass
Upper stack
lower stack

## Slide 4: MRPC in ToF system
MRPC has been widely adopted to construct the Time of Flight (TOF) systems in HEP experiments.
 | ALICE | STAR | FOPI | BESIII | CBM | SoLID
Active area per detector (cm) | 120 x 13 | 22 x 8.4 | 90 x 4.6 | 0.5x(9.2+14.8)x32.8 | 33 x 27.6 | --
Total active area (m2) | 141 | 50 | 5 | 1.33 | 120 | 10
Pad size (cm) | 3.7 x 2.5 | 6.3 x 3.1 | 90 x 0.3 | (9.1~14.1) x 2.4 | 27 x 1.0 | (16~28) x 2.5
Gap×thickness(mm) | 10 x 0.25 | 6 x 0.22 | 6 x 0.3 | 12 x 0.22 | 10 x 0.25 | 32 x 0.128
Gas mixtures (C2H2F4/ C4H10/SF6) | 90/5/5 | 95/5/0 | 85/5/10 | 90/5/5 | 90/5/5 | 90/5/5
Operating field (kV/cm) | 96 | 107 | 110 | 109 | 110 | 140
Efficiency | 99.9% | 95-97% | 97±3% | 99% | 97% | 98%
Time resolution(ps) | 40 | 60 | 73±5 | 60 | 60 | 20 ps
Max rate (Hz/cm2) | 50 | 10 | 50 | 50 | 30k | 20k
higher counting rate and time precision.

## Slide 5: RHIC-STAR TOF system
Long side view
STAR TOF-Tray

## Slide 6: PID and physics success
TOF
TOF PID:
 /k ~1.6 GeV/c,
(,k)/p ~ 3.0 GeV/c
Nature 473 (2011) 353

## Slide 7
PID and physics success
STAR实验在200 GeV金核-金核碰撞中发现底夸克偶素“顺次压低”的实验迹象.
The STAR Collaboration* Phys. Rev. Lett. 130 (2023) 112301
2014年，STAR采用MRPC技术建造了新型的缪子探测器，通过测量双缪子的信号来重建底夸克偶素。MRPC的优秀时间分辨率（70ps）可以压低强子本底，提高双缪子道的时间窗匹配精度。
+-

## Slide 8: Future requirement for MRPC-TOF
High counting rate: >20kHz/cm2
Electrode material, detector structure, spacer…
High time resolution: <20ps
Detector structure, readout electronics (FEE + sampling, TDC…)
Economic and lower gas consumption
Detector structure, eco-gas…

## Slide 9: Higher counting rate: low-resistive glass
low-resistive glass control the voltage drop (efficiency loss) when incident flux goes up by Decrease the resistivity of the electrodes
Low-resistive glass has been operating at FAIR-Phase 0 programs like STAR-eTOF and mCBM
It will be applied in CBM-ToF Wall
Beam test result:
93%, 80ps ,70kHz/cm2
Specifications of low resistive glass
Notes: 在介绍为

## Slide 10: Higher counting rate (<7kHz/cm2): gas pollution
Constant rate condition of 1kHz/cm2
The gas pollution in the gas gap caused the increase of current!
Gas tube
Inlet/outlet
Fishline hook
3D printed sealing frame with Good strength, insulation and radiation persistency
Sealing MRPC speed up gas exchange and can reduce to 1sccm/m2 flush rate at cosmic experiment!

## Slide 11: Excellent performance of sealed MRPC
Sealed MRPC promoted gas exchange
Excellent current behavior under high rate irradiation:
Stable current with constant rate condition.
Fast decay of dark current since when X-ray is off
Decrease the wait time of gas purging:
Reach the working HV in 2h since flowing the gas

## Slide 12: High counting rate (>7kHz/cm2): creepage on fishing line
The creepage on the fishing line caused the high current and deposition!
35 um
fishline contact
Chart: Relaxation time [h]
| 1 | 1 | 2 | 10 | 60 | 120 | 300 | 600 | 1200 | 3600 | 7200 | 14400 | 28800 | 45000
Sparse fishline | 7.58 | 1.21 | 1.15 | 1.15 | 1.14 | 1.13 | 1.09 | 1.04 | 0.95 | 0.78 | 0.65 | 0.52 | 0.37 | 0.27
Dense fishline | 8.55 | 2.69 | 2.64 | 2.64 | 2.61 | 2.58 | 2.51 | 2.4 | 2.25 | 1.93 | 1.7 | 1.47 | 1.23 | 1.05
Chart: Irradiation time [h]
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.8 | 1 | 1.5 | 2 | 3 | 4 | 5 | 6 | 7 | 7.75
Sparse fishline | 6.47 | 6.66 | 6.78 | 6.87 | 6.95 | 7.05 | 7.19 | 7.25 | 7.35 | 7.43 | 7.52 | 7.58 | 7.6 | 7.6 | 7.59 | 7.58
Dense fishline | 6.42 | 6.62 | 6.73 | 6.82 | 6.91 | 6.99 | 7.18 | 7.29 | 7.51 | 7.67 | 7.93 | 8.13 | 8.29 | 8.4 | 8.51 | 8.55
Gas flow
Gas inlet
Gas outlet
Mylar spacer: 3 x 3 x0.25mm
Dark current decay after 10h
@7 kHz/cm2 radiation

## Slide 13: Toward 20ps resolution: narrow gap MRPC
TOF <20 ps， the intrinsic resolution of narrow gaps MRPC is around 15ps，so the time jitter of readout electronics <13~15 ps。
Simulation indicates proper ways to design the gap thickness and arrange the stacks
Narrower gap thickness required
MRPC <20 ps，the gas gap: <0.18mm
gap number: >16

## Slide 14
MRPC
粒子源
固定阈值
传统读出方式：设置固定阈值，得到
  信号过阈时间：
  信号大于阈值的持续时间：
新的读出方式：完整信号波形
新的时间重建算法：使用神经网络挖掘波形规律，给出粒子飞行时间的估计。
过阈甄别
时幅拟合
矫正偏差
固定的一种数据分析模型
输入信息
复杂神经网络
结构变化可能性多
待定参数众多
网络+训练参数
多种可能模型
机器学习
时幅矫正
基于机器学习的MRPC时间重建算法

## Slide 15
ComLSTM (Combined LSTM)：结合FC和LSTM，网络的输入分成两路， 1. 原有LSTM网络（LSTM-420-FC） 2. 先进入FC扩大输入特征维度，再进入一LSTM-400，提取放大后的细节信息
两路输出加权求和后为ComLSTM输出
网络训练：6万模拟数据，输入为上升沿上10个点
改进型comLSTM网络

## Slide 16: Toward 20ps resolution: fast readout electronics
low

## Slide 17: Toward 20ps resolution: fast readout electronics
Fast amplifier & Waveform sampling
Electronic system time σ<7ps
Waveform sampling
Based on DRS4
Sampling freq=5 GS/s
Fast amplifier
Bandwidth=1.4GHz
 | MRPC prototype
gas gap thickness | 128 μm
number of gas gaps | 4 chambers × 8 gaps
glass material | low resistivity glass
glass thickness | 400
readout strips | 5 mm in width (2 mm clearance)
材料厚度：<0.1X0

## Slide 18: Cosmic test
Total time resolution
MRPC + fast amplifier + DRS4
Timing：CFD
Event choose：Vertical cosmic ray
E=140 KV/cm

## Slide 19: 20ps,15kHz/cm2 MRPC
detection efficiency
time resolution
detection efficiency
time resolution
rate
We are also trying with NINOs+ FPGA TDC to get good resolution!

## Slide 20: Sealed MRPC for CEE-eTOF
Cosmic test result:
Gas: 90% F134a+5% Iso-butane + 5% SF6
Efficiency=97%
Time resolution=53ps
N of strips | 32 | 16
N of gaps | 2× 5 | 
Gap thickness(mm) | 0.25 | 
Glass thickness(mm) | 0.7 | 
N of counters | 18 | 6
Active area(mm2) | 480×560 | 480×280
Strip interval(cm) | 1.5+0.2 | 1.5+0.2
Strip length(cm) | 48 | 
CEE-eTOF wall, 5m2, 1500 channels
Gas consumption rate <10sccm/m2 MRPCs at CEE condition.
Notes: 先描述它的结构，再描述它的通气量。
这里也需要注意因为宇宙线实验的计数率很低，如果到束流会怎么样呢？是否需要更高的

## Slide 21
研制技术及研制计划流程
58ps
严格按照研制技术流程进行。

## Slide 22
系统束流实验
2023年4月1日-28日，兰州CSR加速器
Fe-Fe @300AMeV

## Slide 23
束流末端闪烁探测器计数（束流强度） | MRPC工作电流（两个之和）[uA]
199949 | 0.08
517000 | 0.33
1000000 | 0.6
1120000 | 1.2
1600000 | 1.9
Chart: 
| 199949 | 517000 | 1000000 | 1120000 | 1600000
 | 0.08 | 0.33 | 0.6 | 1.2 | 1.9
时间分辨59ps @ 6400V，效率98%，
做了位置修正，通道延时修正，动量修正
双粒子径迹重建, iTOF1+iTOF2+eTOF1+eTOF2
初步实验结果

## Slide 24
24
基于NICA的中俄科技合作
BM@N
applied research area
SPD
MPD
Center NICA
Nuclotron ring (c=251,5 m)
Collider ring (c=503 m)
24
ECal
Present and future HI experiments

## Slide 25
Electromagnetic Calorimeter for NICA/MPD
MPD-ECal requirements:
particle occupancy : < 5%
Time resolution : <1~2ns
Energy resolution : < 5% @1GeV
Operate in the magnetic FIELD : ~ 0.5T
Adequate space resolution.
Cut on time in Ecal (2ns）
具有高时间性能的ECAL能够提高粒子鉴别能力！

## Slide 26
ECAL的组成结构
闪烁体：塑料闪烁体
WLSF： Y11
光电读出： SiPM
均是快响应器件，能够达到高时间分辩

## Slide 27
Spatial resolution
Spatial resolution Vs. energy
Linearity
 | 矫正前后 | 时间分辨[ps]
束流实验 | 时幅矫正前 | 823
 | 时幅矫正后 | 190
模拟结果 | 时幅矫正前 | 469
 | 时幅矫正后 | 146
ECAL模块的性能
时间分辨

## Slide 28
Module production in THU
Module production in SDU
Module production in THU
800个ECAL模块的批量生产
JINR 的接收及装配测试

## Slide 29
220 layer is separated into 4 parts, each part consists of 55 layers
Readout with 32 WLSFs, each part is readout with 8 WLSFs+SiPM
Mask technology of WLSF
5D: x,y,z, energy (5%), time (~50ps)
传统的Shashlyk量能器,没有能量沉积的深度信息
能量沉积的深度分布 + 优秀的时间分辨 大大提高了粒子鉴别能力
五维Shashlyk电磁量能器的概念
e
提高了粒子入射位置和方向精度

## Slide 30: Summary
The rate capability of MRPC assembled with low resistive glass can reach 70kHz/cm2
Sealed MRPC was developed in THU:
Promote gas exchange in gas gap; Prevent creepage @20kHz/cm2 ;Reduce gas consumption greatly. Has been used in CBM-TOF and CEE-eTOF
The time resolution of narrow gap MRPC with fast electronics can be better than 20ps
Shashlyk ECAL can reach:
Energy resolution <5%; Position resolution<5mm; Time resolution <150ps
五维Shashlyk ECAL:
时间分辨可达50ps，还具有深度分度，具有更好的粒子鉴别能力！

## Slide 31
谢谢大家！