## Slide 1
Conceptual design of a novel gaseous scintillation neutron detector for cross-section measurement
Jianqi Chen(陈建琪)，Junsheng Jing(景俊升)，Yongce Gong(贡庸策)
Great Bay University
chenjianqi@gbu.edu.cn
2024/9/8

## Slide 2: Background
How did elements heavier than iron form?
One of greatest unanswered questions of physics
[科学通报, 2022, 67(28):10.]
• Neutron capture reaction is the main path of producing ultra iron elements
, two main neutron source reaction
cs is also important for evaluating dark matter and neutrino detector backgrounds
https://cosmicopia.gsfc.nasa.gov/nucleo.html
Notes: owever, the astrophysical models have yet to adequately reproduce the observed solar abundances of those elements beyond iron(referred to as ultra-iron elements). It is widely believed that these ultra-iron elements were primarily synthesized via the slow neutron capture process(s-process) and the fast neutron capture process(r-process). The fundamental s-process component is thought to originate from thermally pulsing low-mass AGB stars, with reaction pathways closed after the stable nuclides. About half of the heavy elements(up to bismuth) were produced via the s-process. The r-process is thought to occur in the explosive burning of core-collapse supernova and/or neutron-star mergers. Although the r-process site remains a mystery, experts believe that more than half of the ultra-iron elements(up to thorium and uranium) were produced via the r-process.

## Slide 3: Challenge of cs at high neutron energy
[PHYSICAL REVIEW LETTERS 125, 062501 (2020)]
• When cross section measurements by different group differ greatly.
• In addition13C 96Zr 48Ti 50Ti and 76Ge (alpha, n) cross section are also needed.
Status of 13C(alpha, n) 16O cs measurement
Notes: Zirconium titanium Germanium

## Slide 4: cs meas by direct counting method
Neutron detector array
(Sichuan University & IMP)
HeBGB
(Ohio University)
• Polyethylene moderated 3He tube array detectors are widely used for (alpha, n) cross section measurement.
[Nuclear Science and Techniques 33.4 (2022): 41.]
18 BF3 detectors
16 3He detectors
[Journal of Instrumentation 17.05 (2022): P05004]
LERDA
(IMP & CIAE)
[Nuclear Inst. and Methods in Physics Research, A 1003 (2021) 165323.]
• high detection efficiency for thermal neutron
• good n/gamma discrimination
• low price of polyethylene and easy to be designed in different shape

## Slide 5: “Polyethylene+3He” tube detector application
[NIM-A, 1969,72(2):161-166]
cs measurement
cs measurement
cs measurement
delayed neutron
Fission study
Neutron flux monitor
• “Polyethylene +3He tubes” array detectors are widely used in nuclear physics field.
[NIM-A, 2014,99-105]
[NIM-A, 422.1-3, 1999: 43-46]
[Physical Review C 83.6(2011):064617]
[强激光与粒子束,2017,29(12):149-154]
[核技术,2020,43(11):9]

## Slide 6: Performance of “polyethylene+ 3He”detector
BRIKEN Configuration
Detection efficiency vs Neutron energy
[The BRIKEN collaboration, Jinst, 2017, 12]
Compact mode(166 tubes)
3He Volume：
(120 L)@1 atm
• High detection efficiency
• Efficiency is less sensitivity to neuron energy
• Efficiency is less sensitivity to neuron
emission angle
Expected features
Real Performance
• High detection efficiency
• Efficiency heavily depends on neuron energy when >1 MeV
Notes: The aim was to obtain a detection efficiency as high and as constant as possible in the energy range of interest for these neutrons from 1 keV to a few MeV. This constant efficiency is crucial since the information on the initial energy of the neutron will be lost during the moderation process. For neutron-emitters with unknown neutron energy spectrum the same efficiency will be used regardless of neutron energy.

## Slide 7: Response to energy and emission angle
Efficiency vs Neutron energy
Efficiency vs Neutron emission angle
[Journal of Instrumentation 17.05 (2022): P05004.]
[NIM-A 745 (2014): 99-105.]
• When detection efficiency falls clearly except HeBGB detector(flatness 1.17 but with a rather low detection efficiency 7%).
• Efficiency is also sensitive to neutron emission angle, and sensitive region varies with neutron energy.

## Slide 8: Efficiency analysis
Low efficiency reason
• A substantial fraction of thermal neutrons are absorbed by polyethylene.
• 3He tube can’t achieve full coverage of ，partial neutrons may emitted through the 3He tubes gap.
Angle dependency reason
New detector with less sensitivity to neutron energy and angular distribution is required!
Energy dependency reason
• Elastic cross section varies with the neutron energy in the interest region of energy.
• 3He tube can’t achieve full coverage of ，partial neutron emitted through the 3He tube gap.

## Slide 9: Inspiration of new detector design
[William PhD thesis neutron to hidden neutron oscillation in ultracold neutron beam]
CF4+3He/BF3
PMT
PMT
PMT
PMT
PMT
PMT
TMP
Alpha beam
Sample
D2O
Decay time 15 ns,
106 cps
Using heavy water to slow down fast neutron
n + 3He  p + t (Q = 0.764 MeV)
p and t ionize and excite CF4 emit light
Emitted light are detected by surrounding PMTs
[陈建琪,博士论文,基于直接中子法测量93Nb(n,2n)92g+mNb反应截面的实验研究]
“3He+CF4”detector configuration

## Slide 10: Why choose D2O？
Excitation function of H and D
• D has a wider flatness region than H for excitation function curve of elastic scatter.
• The (n, gamma) cross-section of D is 2-3 orders of magnitude lower than that of H, greatly reducing neutron absorption.
• When 3 MeV, it can open the (n, 2n) channel of D, which can significantly increase neutron number to compensate the loss of falling elastic scatter cross section.
[ENDF/B-VIII]

## Slide 11: Optimal configuration
• average detection efficiency
• flatness factor
Software: MCNPX, Emission angle: isotropic distribution
V
[The BRIKEN collaboration, Jinst, 2017, 12]
[Courtesy：Junsheng]
[Courtesy：Junsheng]
Outer radius (cm)
Outer radius (cm)

## Slide 12: Detection efficiency @
• optimal configuration：，，，3He thickness 3.2 cm
CF4+3He
PMT
PMT
PMT
PMT
PMT
PMT
TMP
D2O
•
• Neutron emitted isotropically
configuration
Efficiency vs neutron energy
SOURCE
[Courtesy：Junsheng]

## Slide 13: Detection efficiency@
• After adding 0.8 cm Be, efficiency curve lift a bit, but the valley around 5 MeV still exists.
9Be excitation function
Efficiency vs Neutron energy
[ENDF]
[Courtesy：Junsheng]

## Slide 14: Detection efficiency@
11B excitation function
Efficiency vs Neutron energy
• After adding 6 cm 11B，efficiency drops to 75%，flatness has significant improvement, reaching to 1.02.
[ENDF]
[Courtesy：Junsheng]

## Slide 15: Efficiency angular dependency
3He
D2O
Be
B
PMT
Neutron energy: MeV
Neutron emission angle: and angle with respect to different materials
Run number：
• Efficiency independency angle region: [, ]
• Flatness region independent with neutron energy
Optimal configuration
Efficiency vs Neutron Emission Angle
[Courtesy：Junsheng]
PMT
PMT
PMT
PMT
PMT
PMT
SOURCE

## Slide 16: Performance comparison
Efficiency vs Neutron Energy
Efficiency vs neutron emission angle
• “CF4+3He” gas scintillation detector(6 cm 11B+0.2 cm Be+70 cm+2.8 cm 3He) has a better flatness of 1.02, and detection efficiency as high as 75%.
• “CF4+3He” gas scintillation detector has a wider insensitive angular region.
[Courtesy：Junsheng]
[Courtesy：景俊升]

## Slide 17: Alternative configuration 1-
63Cu excitation function
Efficiency vs Neutron Energy
• After substituting 10 cm natCu by 6 cm 11B, detection efficiency drops to 50%, and flatness curve get worse when
[ENDF]
[Courtesy：Junsheng]

## Slide 18: Alternative configuration 2-
C excitation function
Efficiency vs Neutron energy
• Besides replacing 11B by natCu, also substitute D2O by C(Graphite), detection efficiency drops to 30% and flatness curve still is bad when .
[Courtesy：Junsheng]

## Slide 19: Performance comparison
Efficiency vs Neutron energy
Efficiency vs Neutron emission angle
[Courtesy：Junsheng]
[Courtesy：Junsheng]
Detector/Performance | HeBGB | 11B+B+D2O | natCu+B+D2O | natCu+B+C
Efficiency deviation | 10% | <2% | 10%() | 10%()
Efficiency angle independence region |  | [16,164] | [30,150] | [30,150]
Detector/Performance | HeBGB | 11B+B+D2O | natCu+B+D2O | natCu+B+C
Efficiency deviation | 10% | <2% |  | 
Efficiency angle independence region |  |  |  | 

## Slide 20: Summary
• Merits
• high detection efficiency of 75% and less sensitivity to neutron energy and emission angle.
• less sensitivity to neutron energy, flatness: 1.02.
• less sensitivity to neutron emission angle: independency region:[,]
with respect to the incident beam.
• Demerit
• Volume is big and Cost is high(6 cm11B + 0.2 cm Be +70 cm D2O)
• Two alternative configurations(natCu+Be+D2O and natCu+Be+C) have relative low detection efficiency and a bad flatness when MeV.
• Not consider the contribution of light generation probability and light collection efficiency yet, more simulation and experimental work need to do.

## Slide 21
Thank you!
Welcome to visit GBU!

## Slide 22: Toy Model
3He
PM
PMT
Neutron Source
Polyethylene
5 cm
5 cm
2 cm
Direction: isotropic emission
Run number: 200000
Geometry
• Leaking neutron increase with the increasing neutron energy.
• detection efficiency drops apparently.
 Detection efficiency

## Slide 23: Next work plan
[J. Res. Nat. Inst. Standards Tech. 113, 69 (2008)]
Light Yield : 1000 photon/MeV
[祁辉荣，COUSP2024 CONFERENCE]
[William Master Thesis]
4 atm 3He
1-2 atm CF4

## Slide 24: Toy Model
Geometry
• incident neutron spectrum small difference in thermal neutron region.
• great difference.

## Slide 25: Background
[Matsuda Sayuri’s doctoral thesis (2018, Tohoku University)]
10 tons of 13C in detector
[Juergen Reichenbacher (SDSM&T)]
[PHYSICAL REVIEW LETTERS 125, 062501 (2020)]
[科学通报, 2022, 67(28):10.]
✓ 5.0 MeV以下，测量结果符合的较好
✓ 5.0 MeV以上，测量结果有明显偏差
[ITER，来源于网络]
• D + T → 4He (3.52 MeV) + n (14.1 MeV)
• D + 3He → 4He (3.66 MeV) + p (14.7 MeV)
• P + 11B → 3 4He (8.68 MeV)
~1 MeV (around the Gamow peak)
WIMP & Geo-neutrinos detector background
Nuclear astrophysics
Nuclear technique
[Mark Gilbert, IAEA technical meeting on (alpha, n) nuclear data]
• 16O(n, alpha)13C 反应堆中常见的反应

## Slide 26: CS measurement method
Polyethylene + 3He tubes
Detectors used for direct measurement
Reference | Detector configuration
Sekharan(1967) | Paraffin + BF3 counters
Davids(1968) | Stilbene crystal + scintillation counter
Brune and Kellogg(1993) | Polyethylene + 3He counters
Heil(2008) | BaF2 crystal+ scintillation counter
Droleff(1993) | Polyethylene + 3He counters
[陈涵博士论文，13C(alpha, n)16O深地实验的相关技术研究]
[Nuclear Science and Techniques 33.4 (2022): 41.]

## Slide 27: Status of cs measurement
[Zach Misel, IAEA technical meeting on (alpha,n) nuclear data]

## Slide 28: HeBGB detector
HeBGB detector configuration
[Journal of Instrumentation 17.05 (2022): P05004]
[Zach Meisel, IAEA technical meeting on (alpha, n) nuclear data]
18 BF3 detectors
16 3He detectors