## Slide 1: 缪子探测器和ECAL研究
Yi Wang
Department of Engineering Physics
Tsinghua University

## Slide 2: 谱仪结构

## Slide 3: 缪子TOF探测器
结构及功能：
采用MRPC技术，飞行时间
分辨缪子和介子
飞行时间法：30ps
介质吸收法：<80ps
端部+桶部

## Slide 4: 缪子TOF探测器及吸收体
如果TOF时间分辨达到30ps。的质量为0.139GeV/c2，μ的质量为0.104GeV/c2
要使n=3，则L=1.58m
不同厚度吸收体对和的吸收情况

## Slide 5: 20ps MRPC结构及读出电子学
TOF <20 ps， the intrinsic resolution of narrow gaps MRPC is around 15ps，so the time jitter of readout electronics <13~15 ps。
Simulation indicates proper ways to design the gap thickness and arrange the stacks
Narrower gap thickness required
MRPC <20 ps，the gas gap: <0.18mm
gap number: >16

## Slide 6: Toward 20ps resolution: fast readout electronics
Fast amplifier & Waveform sampling
Electronic system time σ<7ps
Waveform sampling
Based on DRS4
Sampling freq=5 GS/s
Fast amplifier
Bandwidth=1.4GHz
 | MRPC prototype
gas gap thickness | 128 μm
number of gas gaps | 4 chambers × 8 gaps
glass material | low resistivity glass
glass thickness | 400
readout strips | 5 mm in width (2 mm clearance)
材料厚度：<0.1X0

## Slide 7
Total time resolution
MRPC + fast amplifier + DRS4
Timing：CFD
Event choose：Vertical cosmic ray

## Slide 8: 密封式可以大大节省气体消耗量
Constant rate condition of 1kHz/cm2
The gas pollution in the gas gap caused the increase of current!
Gas tube
Inlet/outlet
Fishline hook
3D printed sealing frame with Good strength, insulation and radiation persistency
Sealing MRPC speed up gas exchange and can reduce to 1sccm/m2 flush rate at cosmic experiment!

## Slide 9: HIAF高能谱仪的缪子探测器概念设计
Performance：
1、Time resolution：<35ps
2、PID of /: 500MeV@3
3、Material：0.1X0

## Slide 10: STAR 缪子探测器（MTD）
”Measurement of Sequential Υ Suppression in Au + Au Collisions at √sNN = 200 GeV with the STAR Experiment”
Phys. Rev. Lett. 130 (2023) 112301，2023年3月14日
结果显示出RHIC能区的重离子碰撞中存在底夸克偶素“顺次压低”的实验迹象，表明碰撞中产生的高温介质强烈压制了激发态Υ的产生。该测量对理解高温介质中的强相互作用性质以及提取QGP热力学参数提供了重要实验约束

## Slide 11: HIAF高能谱仪上Ecal
功能及要求：
测量e, , , n等
重建0
横动量: 50MeV-500MeV
时间分辨：<200ps
位置分辨？

## Slide 12: Performance of shashlyk Ecal for NICA/MPD
Parameters of main module |  |  | 
Transverse size, mm2 | 40 x 40 | Scintillator thickness, mm | 1.5
WLS fibers | 16 | Moliere radius, mm | 62
Number of layers | 220 | Radiation length, X0 | 11.8
Lead absorber thickness, mm | 0.3 | Effective radiation length, mm | 32.4

## Slide 13: Performance of shashlyk Ecal for NICA/MPD
1-5GeV
10MeV-350MeV
Spatial resolution Vs. energy
能量分辨率
位置分辨

## Slide 14: The conceptual structure of 5D ECAL
220 layer is separated into 4 parts, each part consists of 55 layers
Readout with 32 WLSFs, each part is readout with 8 WLSFs+SiPM
Mask technology of WLSF
5D: x,y,z, energy (<5%), time (<100ps)

## Slide 15
Electron can be separated from Pion, Proton and Kaon
Neutron can be separated from charged particles by TOF
Neutron energy can be measured by amplitude
PID capability = TOF+ ECal
更准确测量电子伽马的角度
e, 

## Slide 16: 以低能伽马和高能中子分辨为例
模拟了动能1GeV-2GeV的中子和450MeV-550MeV的gamma，筛选出闪烁体中沉积能量在100-150MeV的事例。
鉴别方法如下：设入射粒子在四段闪烁体中沉积能量分别为en (n=1,2,3,4)，etot=e1+e2+e3+e4，an=en/etot (n=1,2,3,4)，利用an做简单判选，图中横轴为判选阈值，当a1,a2,a3均小于阈值且a4小于0.3时判定为gamma，否则判定为中子。

## Slide 17
排除低能γ事例中的中子事例
X、Y、Z轴分别为入射粒子在第1、2、3段中沉积能量占总沉积能量之比
中子沉积能量集中于某一段
低能γ沉积能量集中于前方
γ
中子
X
Y
Z
X
Y
Z

## Slide 18
中子沉积能量集中于某一段
低能γ沉积能量集中于前方
利用入射粒子在各段中沉积能量占比鉴别γ与中子
α错误：将γ事例误认为中子事例
β错误：将中子事例误认为γ事例
后续计划尝试用机器学习方法进行鉴别
α错误率约为2%时， β错误率约为32%
α错误率约为5%时， β错误率约为23%
α错误率约为10%时， β错误率约为18%
排除低能γ事例中的中子事例

## Slide 19: Performance of prototype
19
Transverse size, mm2 | 40×40
Number of layers | 216
Thickness of scintillator, mm | 1.5
Thickness of lead absorber, mm | 0.3
Moliere radius, mm | 62
Number of radiation length, X0 | 11.8
Number of WLS fibers | 16
Shading material | Aluminum ally tubes internal: ϕ1.3mm external: ϕ1.5mm
Time resolution
  Compare with normal Shashlyk ECal:
  356.6 ps →176 ps (Cosmic)

## Slide 20: 3 x 4 Ecal 模块
总共48路读出，12月
参加CEE束流测试，主要测试中子，的响应

## Slide 21
Thanks for your
attention !